## Slide 1
Md. Enamul Haque (MEHq)
enamul.m3h@gmail.com
CSE 1125
Digital Logic Design (CSE 1325)

## Slide 2: Digital Logic Design?
Digital
  Concerned with the interconnection among digital components and modules
  Best Digital System example is General Purpose Computer.
Logic Design
  Deals with the basic concepts and tools used to design digital hardware consisting of logic circuits
  Circuits to perform arithmetic operations (+, -, x, ÷)

## Slide 3: Why it is called Digital Logic Design!
It deals with designing circuits that manipulate digital signals, which are discrete and have two states:
  high (usually representing a logical '1’)
  low (usually representing a logical '0')

## Slide 4: Outline of this lecture
Base conversions
    Decimal ↔ Binary
    Any base → Decimal
    Octal ↔ Binary
    Hexadecimal ↔ Binary
Binary Codes
Binary Coded Decimal (BCD)
Binary arithmetic
    Single Bit Addition with Carry
    Multiple Bit Addition
    BCD Addition

## Slide 5: Numbers system

## Slide 6: Numbers System
231.45 =
Here, 10 is called the radix or base of the number system
In 10-base systems, there are 10 symbols (‘0’, ‘1’, … , ‘9’)
In n-base system, there are n symbols (‘0’, ‘1’, … , ‘n-1’)
In binary (2-base) system, there are 2 symbols (‘0’, and ‘1’)

## Slide 7: Is it possible to create our own number system?
Yes! We can.
n-base system, there are n symbols (0, 1, … , n-1)

## Slide 8: Binary → Decimal
(101.011)2= ( )10
Solution:
(101.011)2= 1 X 22 + 0 X 21 + 1X20 + 0X2-1 + 1X2-2 + 1X2-3
= 4 + 0 + 1 + 0 + +
= (5.365)10

## Slide 9: Binary → Decimal
Try Solving yourself:
(00111.10100)2
(1101.11100)2

## Slide 10: Octal → Decimal
(173.115)8= ( )10
Solution:
(173.115)8= 1 X 82 + 7 X 81 + 3X80 + 1X8-1 + 1X8-2 + 5X8-3
= 64 + 56 + 3 + + +
= (123.150390625)10

## Slide 11: Octal → Decimal
Try Solving yourself
(2331)8
(33215.566)8

## Slide 12: Hexadecimal → Decimal
(A05.2B1)16= ( )10
Solution:
(A05.2B1)16 = A X 162 + 0 X 161 + 5X160 + 2X16-1 + BX16-2 + 1X16-3
= 10 X 162 + 0 X 161 + 5X160 + 2X16-1 + 11X16-2 + 1X16-3 = (2565.168212890625)10

## Slide 13: Hexadecimal → Decimal
Try Solving yourself
(CD421.A232)16
(223B.12C)16

## Slide 14: Decimal → Binary
(233.54)10 =( )2
0.54 * 2 = 1.08  1
0.08 * 2 = 0.16  0
0.16 * 2 = 0.32  0
0.32 * 2 = 0.64  0
0.64 * 2 = 1.28  1
0.28 * 2 = 0.56  0
0.56 * 2 = 1.12  1
0.12 * 2 = 0.24  0
0.24 * 2 = 0.48  0
0.48 * 2 = 0.96  0
0.96 * 2 = 1.92  1
0.92 * 2 = 1.84  1
0
1
(233)10 =(11101001) 2
(0.54)10 =(.100010100011) 2
(233.54)10 =(11101001.100010100011)2

## Slide 15: Decimal → Binary using 2n Digits
(205)10 =( )2
(205)10 =(11001101)2
Decimal | 27 = 128 | 26 = 64 | 25 = 32 | 24 = 16 | 23 = 8 | 22 = 4 | 21 = 2 | 20 = 1
Binary | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1
We can write 205 in this way, how?
205 = 128 + 64+ 8+ 4 +1

## Slide 16: Decimal → Octal
(233.54)10 =( )8
233
8
29
8
1
3
8
5
0
3
0.54 * 8 = 4.32 4
0.32 * 8 = 2.56 2
0.56 * 8 = 4.48 4
0.48 * 8 = 3.84 3
0.84 * 8 = 6.72 6
0.72 * 8 = 5.76 5
(233)10 =(351) 8
(0.54)10 =(.424365) 8
(233.54)10 =(351. 424365)2

## Slide 17: Decimal → Hexa-Decimal
(233.54)10 =( )16
233
16
14
16
9
0
14
E
0.54 * 16 = 8.64  8
0.64 * 16 = 10.24  10 (A)
(233)10 =(E9) 16
(0.54)10 =(.8A) 16
(233.54)10 =(E9. 8A)16

## Slide 18: Numbers in Different Bases

## Slide 19: Octal ↔ Binary
Octal  Binary
  Restate the octal as three binary digits starting at the radix point and going both ways.
Binary  Octal
  Group the binary digits into three-bit groups starting at the radix point and going both ways, padding with zeros as needed in the fractional part.
  Convert each group of three bits to an octal digit.

## Slide 20: Octal ↔ Binary
Octal to Binary:
Restate the octal as three binary digits starting at the radix point and going both ways.
(351)8 =( ) 2
(351)8
011
101
001
(351)8 =(011101001) 2

## Slide 21: Octal ↔ Binary
Octal  Binary
Restate the octal as three binary digits starting at the radix point and going both ways.
(351.721)8 =(?) 2
(351.721)8
011
101
001
(351.721)8 =(011101001.111010001) 2
111
010
001

## Slide 22: Octal ↔ Binary
Binary  Octal
100
001
(1100100.11001)8 =(144.62) 2
Padding with 0
110
(1100100.11001)2 =(?) 8
(1100100.11001)8
010
100
1
4
4
6
2

## Slide 23: Hexa-Decimal ↔ Binary
Hexadecimal  Binary
Binary  Hexadecimal
Restate the Hexadecimal as four binary digits starting at the radix point and going both ways.
Group the binary digits into four-bit groups starting at the radix point and going both ways, padding with zeros as needed in the fractional part.
Convert each group of three bits to a Hexadecimal digit.

## Slide 24: Hexa-Decimal ↔ Binary
Hexadecimal  Binary
Restate the Hexadecimal as four binary digits starting at the radix point and going both ways.
(65.DC)16 =( ) 2
(65.DC)16
0110
0101
(65.DC)16 =(01100101.11011100) 2
1101
1100

## Slide 25: Octal ↔ Binary
Binary  Hexadecimal
0110
0000
(001100101.110111)2 =(065.DC) 16
Padding with 0
1101
(001100101.110111)2 =(?) 16
(001100101.110111)16
1100
0101
0
6
5
D
C

## Slide 26: Octal ↔ Hexadecimal
No Direct Approach!!!!!!
Octal
Binary
Hexadecimal
↔
↔
Convert octal number (635.177)8 into hexadecimal number
Convert the number (19D.3F8)16 into octal number.

## Slide 27: Topic Binary Arithmetic

## Slide 28: Binary Addition
4 Cases
  0 + 0 = 0 Carry=0
  0 + 1 = 1 Carry=0
  1 + 0 = 1 Carry=0
  1 + 1 = 0 Carry=1
Add the Following :
  1 0 1 1 1 + 1 1 0 0 0 1 = ?
  10001 + 11101 = ?
1 0 1 1 1
(+) 1 1 0 0 0 1
1 0 0 1 0 0 0
1 1 0 1 1 1 0
Carry

## Slide 29: Binary Subtraction
4 Cases
  0 - 0 = 0
  0 - 1 = 1 (Borrow)
  1 - 0 = 1
  1 - 1 = 0
Subtract the Following :
  1110 - 111 = ?
  11011 + 10110 = ?
1 1 1 0
(-) 1 1 1
1 1 1
1 1 1 0
Borrow

## Slide 30: Binary Subtraction (2’s Complement)
(12)10 - (8)10 = ( )2
(8)10 = (1000)2
(-8)10 = ?? (No representation)
Representation of a negative number:
Write the number in 8 bit, padding with 0’s the rest bit (MSB)
Toggle all the values (01, 10), which is known as 1’s complement.
Then add (+1) with 1’s complement.
The process is called 2’s complement.

## Slide 31: Binary Subtraction (2’s Complement)
(12)10 - (8)10 = (??)2
(12)10 = (1100)2
(-8)10 = (11111000)2
(12)10 + (-8)10 = (??)2
00001100
(+)11111000
1 00000100
Neglect

## Slide 32: Binary Multiplication
4 Cases
  0 X 0 = 0
  0 X 1 = 0
  1 X 0 = 0
  1 X 1 = 1
Multiply the Following
  1010 X 1011 = ?
1010
(x) 1011
1010
1010X
1101110
11110
0000XX
011110
1010XXX

## Slide 33: Binary Multiplication
4 Cases
  0 X 0 = 0
  0 X 1 = 0
  1 X 0 = 0
  1 X 1 = 1

## Slide 34: Binary Division
Divide 1111100 by 10
Divide 128 by 2

## Slide 35: Binary Division
• Let us divide 128 by 8
• Let us divide 101010 by 110
• Now divide 26 by 5
• Do the same , but in binary : 11010 divided by 101

## Slide 36: Topic Binary Codes

## Slide 37: Binary Numbers and Binary Coding
Flexibility of Representation
• Within constraints below, can assign any binary combination (called a code word) to any data as long as data is uniquely encoded.
Information Types
• Non-numeric
• Greater flexibility since arithmetic operations not applied.
• Not tied to binary numbers
• Numeric
    Must represent range of data needed
    Very desirable to represent data such that simple, straightforward computation for common arithmetic operations permitted
    Tight relation to binary numbers

## Slide 38: Binary Coding ( Non-Numeric)
Color | Binary Number
Red | 000
Green | 001
Orange | 010
Yellow | 011
Blue | 101
Indigo | 110
Violate | 111
Given n binary digits (called bits), a binary code is a mapping from a set of represented elements to a subset of the 2n binary numbers.
Example: A binary code for the seven colors of the rainbow

## Slide 39: Binary Coding ( Non-Numeric)
Color | Binary Number
Red | 000
Green | 001
Orange | 010
Yellow | 011
Blue | 101
Indigo | 110
Violate | 111
Given M elements to be represented by a binary code, the minimum number of bits, n, needed, satisfies the following relationships:
n =
Here M= 7
n = = = | 3 |

## Slide 40: Binary Coding ( Non-Numeric)
Suppose you are using n number of digits, in radix r, there are maximum of rn distinct elements that can be represented.
Examples :
  You can represent 4 elements in radix r = 2 with n = 2 digits: (00, 01, 10, 11).
  You can also represent 4 elements in radix r = 2 with n = 4 digits: (0001, 0010,0100, 1000).

## Slide 41: Binary Coding (Numeric)
Decimal | 8,4,2,1 | Excess 3 | 8,4,-2,-1 | Gray
0 | 0000 | 0011 | 0000 | 0000
1 | 0001 | 0100 | 0111 | 0001
2 | 0010 | 0101 | 0110 | 0011
3 | 0011 | 0110 | 0101 | 0010
4 | 0100 | 0111 | 0100 | 0110
5 | 0101 | 1000 | 1011 | 0111
6 | 0110 | 1001 | 1010 | 0101
7 | 0111 | 1010 | 1001 | 0100
8 | 1000 | 1011 | 1000 | 1100
9 | 1001 | 1100 | 1111 | 1101
There are over 8,000 ways that you can chose 10 elements from the 16 binary numbers of 4 bits. A few are useful:

## Slide 42: Binary Coded Decimal
Each decimal digit is represented by a 4 bit binary number.
10 base system or radix 10 system
It has binary representations for 10 different digits 0 to 9
Weighted code with positional weights 8 4 2 1

## Slide 43: Binary Coded Decimal
Warning: Conversion or Coding?
Do NOT mix up conversion of a decimal number to a binary number with coding a decimal number with a BINARY CODE.
1310 = 11012 (This is conversion)
13 ⇔ 0001|0011 (This is coding)

## Slide 44: Binary Coded Decimal
Decimal | 8,4,2,1
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
Valid
Decimal | 8,4,2,1
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111
Invalid

## Slide 45: Binary Coded Decimal
13 ⇔ 0001|0011
12 ⇔ 0001|0010
156 ⇔ 0001|0101|0110
Representation of a decimal number with Binary Coded Decimals

## Slide 46: Binary Coded Decimal
10100 ⇔ 1 4
1001001 ⇔4 9
BCD number to decimal number

## Slide 47: Binary Coded Decimal
Tradeoffs between binary number and packed BCD (BCD coded number)
BCD takes more storage
Addition takes additional steps
Decimal to BCD does not take much time

## Slide 48: Binary Coded Decimal
Tradeoffs between binary number and packed BCD (BCD coded number)
BCD takes more storage
Addition takes additional steps
Decimal to BCD does not take much time

## Slide 49: BCD Arithmetic

## Slide 50: BCD Arithmetic
448 + 489 = ( )BCD

## Slide 51: BCD Arithmetic
Add 2905BCD to 1897BCD showing carries and digit corrections.
0001 1000 1001 0111
+ 0010 1001 0000 0101

## Slide 52: BCD (Excess 3)
Decimal | 8,4,2,1 | Excess 3
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100
You know how to convert to binary
You know how to add
So, convert to binary and just add 0011 (3)

## Slide 53: BCD Arithmetic (Gray Code)
Discovered by Frank Gray
Unweighted code
Two successive values differ in only 1 bit
Binary numbers are converted to gray code, to reduce switching operations
Also known as Unit distance code

## Slide 54: BCD (Gray Code)
Decimal | Binary | Gray
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111

## Slide 55: Binary to Gray Code
Step1 : Record the MSB as it is
Step 2 : Add the MSB to the next bit, record the sum and neglect the carry
Step 3 : Repeat the process

## Slide 56: Gray Code to Binary
Step1 : Record the MSB as it is
Step 2 : Add MSB to the next bit of Gray code, record the sum and neglect the carry
Step 3 : Repeat the process

## Slide 57: Representation using binary numbers
Try yourself
You want to represent all the countries in the world, using binary numbers. How many bits are required to do so?

## Slide 58: Representation using binary numbers
Try yourself
You want to represent all the countries in the world, using binary numbers. How many bits are required to do so?
Total number of countries = 195
Ans: 8 bits

## Slide 59: Representation using binary numbers
Suppose you have a register that can contain 4 bits, how many elements/ pieces of information can you represent?

## Slide 60: Representation using binary numbers
Suppose you have a register that can contain 4 bits, how many elements/ pieces of information can you represent?
Ans: 2n = 24= 16