## Slide 1: CSE 225: Digital Logic Design Combinational Logic Circuit – Part 1 Salekul Islam United International University

## Slide 2: Overview
Part 1: Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2: Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Part 3: Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs

## Slide 3: In this Lecture
Part 1: Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2: Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Part 3: Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs

## Slide 4: Binary Logic and Gates
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.
We study Boolean algebra as foundation for designing and analyzing digital systems!

## Slide 5: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values.
Variable identifier examples:
  A, B, y, z, or X1 for now
  RESET, START_IT, or ADD1 later

## Slide 6: Logical Operations
The three basic logical operations are:
  AND
  OR
  NOT
AND is denoted by a dot (·).
OR is denoted by a plus (+).
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable.

## Slide 7: Notation Examples
Examples:
  is read “Y is equal to A AND B.”
  is read “z is equal to x OR y.”
  is read “X is equal to NOT A.”
Note: The statement:
  1 + 1 = 2 (read “one plus one equals two”)
is not the same as
  1 + 1 = 1 (read “1 or 1 equals 1”).
=
B
A
Y
×
y
x
z
+
=
A
X
=

## Slide 8: Operator Definitions
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0
=
0
1
=

## Slide 9: Truth Tables
0
1
1
0
X
NOT
X
Z
=
Truth table - a tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: Logic Gate Symbols and Behavior
Logic gates have special symbols:
And waveform behavior in time as follows:

## Slide 11: Logic Diagrams and Expressions
Boolean equations, truth tables and logic diagrams describe the same function!
Truth tables are unique; expressions and logic diagrams are not. This gives flexibility in implementing functions.
X
Y
F
Z
Logic Diagram
Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F
×
+
=

## Slide 12: Boolean Algebra
1.
3.
5.
7.
9.
11.
13.
15.
17.
Commutative
Associative
Distributive
DeMorgan
’
s
2.
4.
6.
8.
X
. 1
X
=
X
. 0
0
=
X . X
X
=
0
=
X . X
An algebraic structure defined on a set of at least two elements, with three binary operators (denoted +, · and ) that satisfies the following basic identities:
10.
12.
14.
16.
X + Y
Y + X
=
(X + Y)
Z
+
X + (Y
Z)
+
=
X(Y +
Z)
XY
XZ
+
=
X + Y
X . Y
=
XY
YX
=
(XY)
Z
X(Y
Z)
=
X
+ YZ
(X + Y)
(X + Z)
=
X . Y
X + Y
=
X
+ 0
X
=
+
X
1
1
=
X + X
X
=
1
=
X + X
X = X

## Slide 13: Some Properties of Identities & the Algebra
The identities above are organized into pairs. These pairs have names as follows:
1-4 Existence of 0 and 1 5-6 Idempotence
7-8 Existence of complement 9 Involution
10-11 Commutative Laws 12-13 Associative Laws
14-15 Distributive Laws 16-17 DeMorgan’s Laws
If the meaning is unambiguous, we leave out the symbol “·”
The dual of an algebraic expression is obtained by interchanging + and · and interchanging 0’s and 1’s.
The identities appear in dual pairs. When there is only one identity on a line the identity is self-dual, i. e., the dual expression = the original expression.

## Slide 14: Proof of DeMorgan’s Laws
+
y
x
x
=
y
×
Proof by truth table is trivial
Similarly it can be proven that
y
x
×
y
x
+
=
Notes: It is important that we do not USE DeMorgan’s Laws in doing this proof. This requires a different proof method. We will show that, x’ . y’, satisfies the definition of the complement of (x + y), defined as (x + y)’ by DeMorgan’s Law.
To show this we need to show that A + A’ = 1 and A.A’ = 0 with A = x + y and A’ = x’. y’. This proves that x’. y’ = (x + y)’.
Part 1: Show x + y + x’. y’ = 1.
x + y + x’. y’
= (x + y + x’) (x + y + y’) X + YZ = (X + Y)(X + Z) (Distributive Law)
= (x + x’ + y) (x + y + y’) X + Y = Y + X (Commutative Law)
= (1 + y)(x + 1) X + X’ = 1
= 1 . 1 1 + X = 1
= 1 1 . X = 1
Part 2: Show (x + y) . x’. y’ = 0.
(x + y) . x’. y’
= (x . x’. y’ + y . x’. y’) X (Y + Z) = XY + XZ (Distributive Law)
= (x . x’. y’ + y . y’ . x’) XY = YX (Commutative Law)
= (0 . y’ + 0 . x’) X . X’ = 0
= (0 + 0) 0 . X = 0
= 0 X + 0 = X (With X = 0)
Based on the above two parts, x’y’ = (x + y)’
The second DeMorgans’ law is proved by duality. Note that DeMorgan’s Law, given as an identity is not an axiom in the sense that it can be proved using the other identities.

## Slide 15: Some Properties of Identities Algebra
Unless it happens to be self-dual, the dual of an expression does not equal the expression itself.
Example: F = (A + C) · B + 0
dual F = (A · C + B) · 1 = A · C + B
Example: G = X · Y + (W + Z)
dual G =
Example: H = A · B + A · C + B · C
dual H =
Are any of these functions self-dual?
Notes: Dual G = ((X+Y) · (W · Z)') = ((X+Y) ·(W' + Z')
Dual H = (A + B)(A + C)(B + C). Using the Boolean identities,
= (A +BC) (B+C) = AB + AC + BC. So H is self-dual.

## Slide 16: Boolean Operator Precedence
The order of evaluation in a Boolean expression:
1.
Parentheses
2.
NOT
3.
AND
4.
OR
Consequence: Parentheses appear around
OR expressions
Example: F = A(B + C)(C + D)

## Slide 17: Example 1: Boolean Algebraic Proof
A + A·B = A (Absorption Theorem)
Proof Steps Justification (identity or theorem)
A + A·B
= A · 1 + A · B X = X · 1
= A · ( 1 + B) X · Y + X · Z = X ·(Y + Z)(Distributive Law)
= A · 1 1 + X = 1
= A X · 1 = X
Our primary reason for doing proofs is to learn:
  Careful and efficient use of the identities and theorems of Boolean algebra, and
  How to choose the appropriate identity or theorem to apply to make forward progress, irrespective of the application.

## Slide 18: Example 2: Boolean Algebraic Proofs
AB + AC + BC = AB + AC (Consensus Theorem)
Proof Steps Justification (identity or theorem)
AB + AC + BC
= AB + AC + 1 · BC ?
= AB +AC + (A + A) · BC ?
=
Notes: Justification 1: 1 . X = X
Justification 2: X + X’ = 1
= AB + A’C + ABC + A’BC X(Y + Z) = XY + XZ (Distributive Law)
= AB + ABC + A’C + A’BC X + Y = Y + X (Commutative Law)
= AB . 1 + ABC + A’C . 1 + A’C . B X . 1 = X, X . Y = Y . X (Commutative Law)
= AB (1 + C) + A’C (1 + B) X(Y + Z) = XY +XZ (Distributive Law)
= AB . 1 + A’C . 1 = AB + A’C X . 1 = X

## Slide 19: Example 3: Boolean Algebraic Proofs
Proof Steps Justification (identity or theorem)
=
Y
X
Z
)
Y
X
(
+
+
)
Z
X
(
X
Z
)
Y
X
(
+
=
+
+
Y
Y
Notes: = X’ Y’ Z + X Y’ (A + B)’ = A’ . B’ (DeMorgan’s Law)
= Y’ X’ Z + Y’ X A . B = B . A (Commutative Law)
= Y’ (X’ Z + X) A(B + C) = AB + AC (Distributive Law)
= Y’ (X’ + X)(Z + X) A + BC = (A + B)(A + C) (Distributive Law)
= Y’ . 1 . (Z + X) A + A’ = 1
= Y’ (X + Z) 1 . A = A, A + B = B + A (Commutative Law)

## Slide 20: Useful Theorems
(
)
tion
Simplifica
y
x
y
x
y
x
y
x
×
=
+
×
+
=
×
+
x
x
x
y
×
y
Laws
s
DeMorgan'
x
x
×
=
+
y
x
=
+
y

## Slide 21: Boolean Function Evaluation
z
x
y
x
F4
x
z
y
x
z
y
x
F3
x
F2
xy
F1
+
=
+
=
=
=
z
y
z
+
y
+
Notes: F3 is 1 for x’y’z’, x’yz, xy’z’ and xy’z => F3 = 1,0,0,1,1,1,0,0
F4 is 1 for xy’z’, xy’z, x’y’z and x’y z => F4 = 0,1,0,1,1,1,0,0

## Slide 22: Expression Simplification
An application of Boolean algebra
Simplify to contain the smallest number of literals (complemented and uncomplemented variables):
= AB + ABCD + A C D + A C D + A B D
= AB + AB(CD) + A C (D + D) + A B D
= AB + A C + A B D = B(A + AD) +AC
= B (A + D) + A C 5 literals
+
+
+
+
D
C
B
A
D
C
A
D
B
A
D
C
A
B
A

## Slide 23: Expression Simplification (practice)
X’Y’ + X’Y + XY = X’ + Y
XY + X’Z + YZ = XY + X’Z
ABC’ + BC’D’ + BC + C’D = B+C’D’
((CD)’ + A’)’ + A + CD + AB => Convert it into 3 literals
X’Y’ + XYZ+X’Y => Convert it into 3 literals

## Slide 24: Complementing Functions
Use DeMorgan's Theorem to complement a function:
  1. Interchange AND and OR operators
  2. Complement each constant value and literal
Example: Complement F =
F = =
=(x + y + z).(x + y + z)
Example: Complement G = (a + bc)d + e
G =
x
+
z
y
z
y
x
x
+
z
y
z
y
x
x
z
y
z.
y
x

## Slide 25: Complementing using Dual
Take dual of the function
Then complement each literal
Now complement F = using dual
x
+
z
y
z
y
x

## Slide 26: Where we are?
Part 1: Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2: Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Part 3: Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs

## Slide 27: Overview – Canonical Forms
What are Canonical Forms?
Minterms and Maxterms
Index Representation of Minterms and Maxterms
Sum-of-Minterm (SOM) Representations
Product-of-Maxterm (POM) Representations
Representation of Complements of Functions
Conversions between Representations

## Slide 28: Canonical Forms
It is useful to specify Boolean functions in a form that:
  Allows comparison for equality.
  Has a correspondence to the truth tables
Canonical Forms in common usage:
  Sum of Minterms (SOM)
  Product of Maxterms (POM)

## Slide 29: Minterms
Minterms are AND terms with every variable present in either true or complemented form.
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., ), there are 2n minterms for n variables.
Example: Two variables (X and Y)produce 2 x 2 = 4 combinations:
  (both normal)
  (X normal, Y complemented)
  (X complemented, Y normal)
  (both complemented)
Thus there are four minterms of two variables.
How many for 3 or 4 variables?
Y
X
XY
Y
X
Y
X
x

## Slide 30: Maxterms
Maxterms are OR terms with every variable in true or complemented form.
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., x), there are 2n maxterms for n variables.
Example: Two variables (X and Y) produce 2 x 2 = 4 combinations:
  (both normal)
  (x normal, y complemented)
  (x complemented, y normal)
  (both complemented)
How many for 3 or 4 variables?
Y
X
+
Y
X
+
Y
X
+
Y
X
+

## Slide 31: Maxterms and Minterms
Examples: Two variable minterms and maxterms.
The index above is important for describing which variables in the terms are true and which are complemented.
Index | Minterm | Maxterm
0 | x y | x + y
1 | x y | x + y
2 | x y | x + y
3 | x y | x + y
M0
M1
M2
M3
m0
m1
m2
m3

## Slide 32: Standard Order
Minterms and maxterms are designated with a subscript
The subscript is a number, corresponding to a binary pattern
The bits in the pattern represent the complemented or normal state of each variable listed in a standard order.
All variables will be present in a minterm or maxterm and will be listed in the same order (usually alphabetically)
Example: For variables a, b, c:
  Maxterms: (a + b + c), (a + b + c)
  Terms: (b + a + c), a c b, and (c + b + a) are NOT in standard order.
  Minterms: a b c, a b c, a b c
  Terms: (a + c), b c, and (a + b) do not contain all variables

## Slide 33: Purpose of the Index
The index for the minterm or maxterm, expressed as a binary number, is used to determine whether the variable is shown in the true form or complemented form.
For Minterms:
  “1” means the variable is “Not Complemented” and
  “0” means the variable is “Complemented”.
For Maxterms:
  “0” means the variable is “Not Complemented” and
  “1” means the variable is “Complemented”.

## Slide 34: Index Example in Three Variables
Example: (for three variables)
Assume the variables are called X, Y, and Z.
The standard order is X, then Y, then Z.
The Index 0 (base 10) = 000 (base 2) for three variables). All three variables are complemented for minterm 0 ( ) and no variables are complemented for Maxterm 0 (X,Y,Z).
  Minterm 0, called m0 is .
  Maxterm 0, called M0 is (X + Y + Z).
  Minterm 6 ?
  Maxterm 6 ?
Z
,
Y
,
X
Z
Y
X
Notes: m6 = X Y Z’
M6 = (X’ + Y’ + Z)

## Slide 35: Index Examples – Four Variables
Index Binary Minterm Maxterm
i Pattern mi Mi
0 0000
1 0001
3 0011
5 0101
7 0111
10 1010
13 1101
15 1111
d
c
b
a
d
c
b
a
d
c
b
a
+
+
+
d
c
b
a
d
c
b
a
+
+
+
d
c
b
a
+
+
+
d
c
b
a
d
c
b
a
+
+
+
d
b
a
d
c
b
a
+
+
+
?
?
?
?
c
d
b
a
c
Notes: M1 = a + b + c + d’
m3 = a’ b’ c d
m7 = a’ b c d
M 13 = a’ + b’ + c + d’

## Slide 36: Minterm and Maxterm Relationship
Review: DeMorgan's Theorem
and
Two-variable example:
and
Thus M2 is the complement of m2 and vice-versa.
Since DeMorgan's Theorem holds for n variables, the above holds for terms of n variables
giving:
and
Thus Mi is the complement of mi.
y
x
y
·
x
+
=
y
x
y
x
×
=
+
y
x
M
2
+
=
y
x·
m
2
=
i
m
M
=
i
i
i
M
m
=

## Slide 37: Function Tables for Both
Minterms of Maxterms of
2 variables 2 variables
Each column in the maxterm function table is the complement of the column in the minterm function table since Mi is the complement of mi.
x y
m
0
m
1
m
2
m
3
0 0
1
0
0
0
0 1
0
1
0
0
1 0
0
0
1
0
1 1
0
0
0
1
x y
M
0
M
1
M
2
M
3
0 0
0
1
1
1
0 1
1
0
1
1
1 0
1
1
0
1
1 1
1
1
1
0

## Slide 38: Observations
In the function tables:
  Each minterm has one and only one ‘1’ present in the 2n terms (a minimum of 1s). All other entries are ‘0’.
  Each maxterm has one and only one ‘0’ present in the 2n terms All other entries are ‘1’ (a maximum of 1s).
We can implement any function by "ORing" the minterms corresponding to "1" entries in the function table. These are called the minterms of the function.
We can implement any function by "ANDing" the maxterms corresponding to "0" entries in the function table. These are called the maxterms of the function.
This gives us two canonical forms:
  Sum of Minterms (SOM)
  Product of Maxterms (POM)
for stating any Boolean function.

## Slide 39: Minterm Function Example
x y z
index
m1
+
m4
+
m7
= F1
0 0 0
0
0
+
0
+
0
= 0
0 0 1
1
1
+
0
+
0
= 1
0 1 0
2
0
+
0
+
0
= 0
0 1 1
3
0
+
0
+
0
= 0
1 0 0
4
0
+
1
+
0
= 1
1 0 1
5
0
+
0
+
0
= 0
1 1 0
6
0
+
0
+
0
= 0
1 1 1
7
0
+
0
+
1
= 1
Example: Find F1 = m1 + m4 + m7
F1 = x y z + x y z + x y z

## Slide 40: Minterm Function Example
F(A, B, C, D, E) = m2 + m9 + m17 + m23
F(A, B, C, D, E) =
Notes: F(A,B,C,D,E) = A’B’C’DE’ + A’BC’D’E + AB’C’D’E + AB’CDE

## Slide 41: Maxterm Function Example
Example: Implement F1 in maxterms:
F1 = M0 · M2 · M3 · M5 · M6
)
z
y
z)·(x
y
·(x
z)
y
(x
F
1
+
+
+
+
+
+
=
z)
y
x
)·(
z
y
x
·(
+
+
+
+
x y z
i
M0

M2

M3

M5

M6
= F1
0 0 0
0
0
1
1
1
= 0
0 0 1
1
1
1
1
1
1
= 1
0 1 0
2
1
0
1
1
1
= 0
0 1 1
3
1
1
0
1
1
= 0
1 0 0
4
1
1
1
1
1
= 1
1 0 1
5
1
1
1
0
1
= 0
1 1 0
6
1
1
1
1
0
= 0
1 1 1
7
1








1
1
1
1
= 1
1

























## Slide 42: Maxterm Function Example
F(A, B,C,D) =
14
11
8
3
M
M
M
M
)
D
,
C
,
B
,
A
(
F
×
×
×
=
Notes: F = (A + B + C’ + D’) (A’ + B + C + D) (A’ + B + C’ + D’) (A’ + B’ + C’ + D)

## Slide 43: Canonical Sum of Minterms
Any Boolean function can be expressed as a Sum of Minterms.
  For the function table, the minterms used are the terms corresponding to the 1's
  For expressions, expand all terms first to explicitly list all minterms. Do this by “ANDing” any term missing a variable v with a term ( ).
Example: Implement as a sum of minterms.
  First expand terms:
  Then distribute terms:
  Express as sum of minterms: f = m3 + m2 + m0
y
x
x
f
+
=
y
x
)
y
y
(
x
f
+
+
=
y
x
y
x
xy
f
+
+
=
v
v
+

## Slide 44: Another SOM Example
Example:
There are three variables, A, B, and C which we take to be the standard order.
Expanding the terms with missing variables:
Collect terms (removing all but one of duplicate terms):
Express as SOM:
C
B
A
F
+
=
Notes: F = A(B + B’)(C + C’) + (A + A’) B’ C
= ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
= ABC + ABC’ + AB’C + AB’C’ + A’B’C
= m7 + m6 + m5 + m4 + m1 = m1 + m4 + m5 + m6 + m7

## Slide 45: Shorthand SOM Form
From the previous example, we started with:
We ended up with:
F = m1 + m4 + m5 + m6 + m7
This can be denoted in the formal shorthand:
Note that we explicitly show the standard variables in order and drop the “m” designators.
C
B
A
F
+
=

## Slide 46: Canonical Product of Maxterms
Any Boolean Function can be expressed as a Product of Maxterms (POM).
  For the function table, the maxterms used are the terms corresponding to the 0's.
  For an expression, expand all terms first to explicitly list all maxterms. Do this by first applying the second distributive law , “ORing” terms missing variable v with a term equal to and then applying the distributive law again.
Example: Convert to product of maxterms:
  Apply the distributive law:
  Add missing variable z:
  Express as POM: f = M2 · M3
y
x
x
)
z
,
y
,
x
(
f
+
=
y
x
)
y
(x
1
)
y
)(x
x
(x
y
x
x
+
=
+
×
=
+
+
=
+
(
)
z
y
x
)
z
y
x
(
z
z
y
x
+
+
+
+
=
×
+
+
v
v
×

## Slide 47: Another POM Example
Convert to Product of Maxterms:
Use x + y z = (x+y)·(x+z) with , and to get:
Then use to get:
and a second time to get:
Rearrange to standard order,
to give f = M5 · M2
B
A
C
B
C
A
C)
B,
f(A,
+
+
=
B
z
=
)
B
C
B
C
)(A
A
C
B
C
(A
f
+
+
+
+
=
y
x
y
x
x
+
=
+
)
B
C
C
)(A
A
BC
C
(
f
+
+
+
+
=
)
B
C
)(A
A
B
C
(
f
+
+
+
+
=
C)
B
)(A
C
B
A
(
f
+
+
+
+
=
A
y
C),
B
(A
x
=
+
=
C

## Slide 48: Function Complements
The complement of a function expressed as a sum of minterms is constructed by selecting the minterms missing in the sum-of-minterms canonical forms.
Alternatively, the complement of a function expressed by a Sum of Minterms form is simply the Product of Maxterms with the same indices.
Example: Given
)
7
,
5
,
3
,
1
(
)
z
,
y
,
x
(
F
m
S
=
)
6
,
4
,
2
,
0
(
)
z
,
y
,
x
(
F
m
S
=
)
7
,
5
,
3
,
1
(
)
z
,
y
,
x
(
F
M
P
=

## Slide 49: Conversion Between Forms
To convert between sum-of-minterms and product-of-maxterms form (or vice-versa) we follow these steps:
  Find the function complement by swapping terms in the list with terms not in the list.
  Change from products to sums, or vice versa.
Example:Given F as before:
Form the Complement:
Then use the other form with the same indices – this forms the complement again, giving the other form of the original function:
)
6
,
4
,
2
,
0
(
)
z
,
y
,
x
(
F
m
S
=

## Slide 50: Standard Forms
Standard Sum-of-Products (SOP) form: equations are written as an OR of AND terms
Standard Product-of-Sums (POS) form: equations are written as an AND of OR terms
Examples:
  SOP:
  POS:
These “mixed” forms are neither SOP nor POS
B
C
B
A
C
B
A
+
+
C
·
)
C
B
(A
·
B)
(A
+
+
+
C)
(A
C)
B
(A
+
+
B)
(A
C
A
C
B
A
+
+

## Slide 51: Standard Sum-of-Products (SOP)
A sum of minterms form for n variables can be written down directly from a truth table.
  Implementation of this form is a two-level network of gates such that:
  The first level consists of n-input AND gates, and
  The second level is a single OR gate (with fewer than 2n inputs).
This form often can be simplified so that the corresponding circuit is simpler.

## Slide 52: Standard Sum-of-Products (SOP)
A Simplification Example:
Writing the minterm expression:
F = A B C + A B C + A B C + ABC + ABC
Simplifying:
F =
Simplified F contains 3 literals compared to 15 in minterm F
Notes: F = A’ B’ C + A (B’ C’ + B C’ + B’ C + B C)
= A’ B’ C + A (B’ + B) (C’ + C)
= A’ B’ C + A.1.1
= A’ B’ C + A
= B’C + A

## Slide 53: AND/OR Two-level Implementation of SOP Expression
The two implementations for F are shown below – it is quite apparent which is simpler!

## Slide 54: SOP and POS Observations
The previous examples show that:
  Canonical Forms (Sum-of-minterms, Product-of-Maxterms), or other standard forms (SOP, POS) differ in complexity
  Boolean algebra can be used to manipulate equations into simpler forms.
  Simpler equations lead to simpler two-level implementations
Questions:
  How can we attain a “simplest” expression?
  Is there only one minimum cost circuit?
  The next part will deal with these issues.