## Slide 2: Overview
Part 1 – Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2 – Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Part 3 – Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates

## Slide 3: Other Gate Types
Why?
  Implementation feasibility and low cost
  Power in implementing Boolean functions
  Convenient conceptual representation
Gate classifications
  Primitive gate - a gate that can be described using a single primitive operation type (AND or OR) plus an optional inversion(s).
  Complex gate - a gate that requires more than one primitive operation type for its description
Primitive gates will be covered first

## Slide 4: Buffer
A buffer is a gate with the function F = X:
In terms of Boolean function, a buffer is the same as a connection!
So why use it?
  A buffer is an electronic amplifier used to improve circuit voltage levels and increase the speed of circuit operation.
X
F

## Slide 5: NAND Gate
The basic NAND gate has the following symbol, illustrated for three inputs:
  AND-Invert (NAND)
NAND represents NOT AND, i. e., the AND function with a NOT applied. The symbol shown is an AND-Invert. The small circle (“bubble”) represents the invert function.
X
Y
Z
Z
Y
X
)
Z
,
Y
,
X
(
F
×
×
=

## Slide 6: NAND Gates (continued)
Applying DeMorgan's Law gives Invert-OR (NAND)
This NAND symbol is called Invert-OR, since inputs are inverted and then ORed together.
AND-Invert and Invert-OR both represent the NAND gate. Having both makes visualization of circuit function easier.
A NAND gate with one input degenerates to an inverter.
X
Y
Z
Z
Y
X
)
Z
,
Y
,
X
(
F
+
+
=

## Slide 7: NAND Gates (continued)
The NAND gate is the natural implementation for the simplest and fastest electronic circuits
Universal gate - a gate type that can implement any Boolean function.
The NAND gate is a universal gate as shown in Figure 2-30 of the text.
NAND usually does not have a operation symbol defined since
  the NAND operation is not associative, and
  we have difficulty dealing with non-associative mathematics!

## Slide 8: Implementing with NAND only
Assume that all variables and their complements are available as inputs.
Find the minimum SOP expression of the function.
Draw the corresponding two-level AND-OR circuit diagram.
Replace all gates with NAND gates; learning the gates interconnections are kept unchanged.

## Slide 9: Implementing with NAND only
Implement the function F using only NAND gates

## Slide 10: Example: Implementing with NAND only

## Slide 11: NOR Gate
The basic NOR gate has the following symbol, illustrated for three inputs:
  OR-Invert (NOR)
NOR represents NOT - OR, i. e., the OR function with a NOT applied. The symbol shown is an OR-Invert. The small circle (“bubble”) represents the invert function.
X
Y
Z
Z
Y
X
)
Z
,
Y
,
X
(
F
+
+
=

## Slide 12: NOR Gate (continued)
Applying DeMorgan's Law gives Invert-AND (NOR)
This NOR symbol is called Invert-AND, since inputs are inverted and then ANDed together.
OR-Invert and Invert-AND both represent the NOR gate. Having both makes visualization of circuit function easier.
A NOR gate with one input degenerates to an inverter.
X
Y
Z

## Slide 13: NOR Gate (continued)
The NOR gate is another natural implementation for the simplest and fastest electronic circuits
The NOR gate is a universal gate
NOR usually does not have a defined operation symbol since
  the NOR operation is not associative, and
  we have difficulty dealing with non-associative mathematics!

## Slide 14: Exclusive OR/ Exclusive NOR
The eXclusive OR (XOR) function is an important Boolean function used extensively in logic circuits.
The XOR function may be;
  implemented directly as an electronic circuit (truly a gate) or
  implemented by interconnecting other gate types (used as a convenient representation)
The eXclusive NOR function is the complement of the XOR function
By our definition, XOR and XNOR gates are complex gates.

## Slide 15: Exclusive OR/ Exclusive NOR
Uses for the XOR and XNORs gate include:
  Adders/subtractors/multipliers
  Counters/incrementers/decrementers
  Parity generators/checkers
Definitions
  The XOR function is:
  The eXclusive NOR (XNOR) function, otherwise known as equivalence is:
Strictly speaking, XOR and XNOR gates do no exist for more that two inputs. Instead, they are replaced by odd and even functions.
Y
X
Y
X
Y
X
+
=
Å
Y
X
Y
X
Y
X
+
=
Å

## Slide 16: Truth Tables for XOR/XNOR
Operator Rules: XOR XNOR
The XOR function means:
X OR Y, but NOT BOTH
Why is the XNOR function also known as the equivalence function, denoted by the operator ?
X
Y
X
Å
Y
0
0
0
0
1
1
1
0
1
1
1
0
X
Y
0
0
1
0
1
0
1
0
0
1
1
1
or X
º
Y
(X
Å
Y)
Notes: Because it is defined as X Y + X’ Y’ that equals 1 if and only if X = Y implying X is equivalent to Y.

## Slide 17: XOR/XNOR (Continued)
The XOR function can be extended to 3 or more variables. For more than 2 variables, it is called an odd function or modulo 2 sum (Mod 2 sum), not an XOR:
The complement of the odd function is the even function.
The XOR identities:
=
=
X
1
X
X
0
X
Å
Å
1
X
X
0
X
X
=
Å
=
Å
X
Y
Y
X
Å
=
Å
Z
Y
X
)
Z
Y
(
X
Z
)
Y
X
(
Å
Å
=
Å
Å
=
Å
Å
+
+
+
=
Å
Å
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X

## Slide 18: Symbols For XOR and XNOR
XOR symbol:
XNOR symbol:
Symbols exist only for two inputs

## Slide 19: XOR Implementations
The simple SOP implementation uses the following structure:
A NAND only implementation is:
X
Y
X
Y
X
Y
X
Y

## Slide 20: Terms of Use
© 2004 by Pearson Education,Inc. All rights reserved.
The following terms of use apply in addition to the standard Pearson Education Legal Notice.
Permission is given to incorporate these materials into classroom presentations and handouts only to instructors adopting Logic and Computer Design Fundamentals as the course text.
Permission is granted to the instructors adopting the book to post these materials on a protected website or protected ftp site in original or modified form. All other website or ftp postings, including those offering the materials for a fee, are prohibited.
You may not remove or in any way alter this Terms of Use notice or any trademark, copyright, or other proprietary notice, including the copyright watermark on each slide.
Return to Title Page